## Slide 1: DIALYSIS MODALITIES OVERVIEW
Conventional Hemodialysis
Online Hemofiltration
Online Hemodiafiltration
Expanded hemodialysis
Acetate free bio filtration (AFB)
Sorbent Dialysis

## Slide 2: Conventional hemodialysis
Most commonly used modality
Simple diffusion based therapy
Only dialysis fluid(dialysate) is required
Water treatment system to provide dialysis quality water as per ISO 13959 standards
Low flux (F6/F8) &high flux dialyzers (Fx60/Fx80/F80s)can be used
Best suitable for small molecular weight removal
2 to3 times/week
4 hours duration treatment

## Slide 3: Online Hemofiltration(online hf)
Pure convection(solvent drag) based technique.
High flux dialyzer is required .
No dialysate is required.
Sterile substitution/replacement Fluid is required.
Machine can produce sterile substitution Fluid during treatment –Hence the name “Online “!
HF offers superior clearance of middle sized uremic solutes (example:B2M,P-Cresoletc)
HF can be applied in 2Configurations:
1) pre-dilution HDF
2)Post-dilution HDF
3) Mixed -dilution HDF

## Slide 4: Expand hemodialysis(HDx)
An innovation hemodialysis technique.
Requres a special MCO ( medium cut off) Dialyzer / Filter with HMRO (High Molcular weight retention Onset)such A Theranova 400 by Baxter Inc.
No special Machine is required .Can be performed in a normal hemodialysis Machine (EX4008S /Dialog +/Surdia /Diamax etc).
These Filters have a MWCO of of Approx 45000 Da with minimal or no protein loss.
Superior medium to larger molecular weight uremic toxins by simple Diffussion.
Not yet commercially introdution in the Market
Still Need Study/ Trials to prove efficacy in MHD patients.

## Slide 5: Acetate free biofiltration(afb)
AFB is a HFD modality with some improvisations.
An OL-HDF Machine is required.
A hollow fiber AN69 Membrane is usually used for AFB for better endotoxin retention by adsorption.
A Buffer Free dialysate is used &145mmol/L sterile NaHCo3 solution is administered 8 to 10 Liters /session in post –Dilution Mode.
Benefits of AFB are :Superior cardiovascular stability ,higher Albumin level , better correction of Acidosis, superior clearance of small& middle molecules.

## Slide 6: Sorbent dialysis
Not a sigle pass Dialysate delivery system.
Reuse of fixed volume Dialysate.
Only 6L Tap water is required for 4 hours HD session .
Machine uses disposable cartridge for dialysate purification during treatment .
R.O systems not required .
Machine purifies the used dialysate using a zirconium based cartridge and adds concentrted electrolytes (called infusate ) to prepare fresh dialysate . This cycle repeats throughout the treatment .
High efficiency in terms of water consumption.